## Slide 1
Reviewer for the final exams(analog part)
Read all the lecture slides carefully
Read the digital part home work questions and their resolutions(digital part)
Read the review for the digital part

## Slide 2
Transistor
n-MOS
p-MOS
  M1 for within-cell routing
  M2 for vertical routing between cells
  M3 for horizontal routing between cells
STI: Shallow trench isolation
AMI 0.6 mm process has 3 metal layers
W: Tungsten

## Slide 3
Transistor: NMOS
VG=VTH
VDS <<2(VGS − VTH),
overdrive voltage: VGS − VTH
With the condition, VDS <<2(VGS − VTH), we say the device operates in the deep triode region.
Deep triode region

## Slide 4
Small signal models
[in saturation]
gm represents the sensitivity of the device: for a high gm, a small change in VGS results in a large change in ID.

## Slide 5: Small signal models
Owing to channel-length modulation, the drain current also varies with the drain-source voltage
The bulk potential influences the threshold voltage and hence the gate-source overdrive
η = gmb/gm and is typically around 0.25.

## Slide 6: Complete MOS small-signal

## Slide 7
Common Source Amplifier

## Slide 8
Common Source Amplifier
For large values of RD, the effect of channel-length modulation in M1 becomes significant

## Slide 9
CS Amplifier: Current-Source Load
In applications requiring a large voltage gain in a single stage, the relationship Av = −gm RD suggests that we should increase the load impedance of the CS stage. With a resistor or diode-connected load, however, increasing the load resistance translates to a large dc drop across the load, thereby limiting the output voltage swing.

## Slide 10
CS Amplifier: Active Load
PMOS Amplifier
The PMOS device serves as a constant current source
PMOS M2 to operate as an amplifying device

## Slide 11
CS Amplifier: Diode Load
In some CMOS technologies, it is difficult to fabricate resistors with tightly controlled values or a reasonable physical size. Consequently, it is desirable to replace RD with a MOS transistor

## Slide 12
Source Follower

## Slide 13
Source Follower: Application
Our analysis of the common-source stage indicates that, to achieve a high voltage gain with limited supply voltage, the load impedance must be as large as possible. If such a stage is to drive a low-impedance load, then a “buffer” must be placed after the amplifier so as to drive the load with negligible reduction in gain. The source follower (also called the “common-drain” stage) can operate as a voltage buffer.

## Slide 14
SF Biasing example (I)
(a) In the circuit of Fig. 3.47(a), calculate the voltage gain if C1 acts as an ac short at the frequency of interest. What is the maximum dc level of the input signal for which M1 remains saturated? (b) To accommodate an input dc level close to VDD, the circuit is modified as shown in Fig. 3.47(b). What relationship between the gate-source voltages of M2 and M3 guarantees that M1 is saturated?
Design of Analog CMOS Integrated Circuits Behzad Razavi
2nd Edition, page 74-75

## Slide 15
SF Biasing example (II)
Design of Analog CMOS Integrated Circuits Behzad Razavi
2nd Edition, page 69-70

## Slide 16
Current Mirror
MREF is always in saturation

## Slide 17
Current Mirror biasing
?
What happens here?
SF Amplifier
CS Amplifier
This circuit is not a current mirror because only a diode-connected device can establish and hence a copy current independent of device parameters and temperature. Since the gates of MREF and M1 are floating, they can assume any voltage, e.g., an initial condition created at node X when the power supply is turned on. In other words, Icopy is very poorly defined.

## Slide 18
Current Mirror biasing
An integrated circuit employs the source follower and the common-source stage shown below. Design a current mirror that produces I1 and I2 from a 0.3-mA reference

## Slide 19
Two-Stage CMOS Op Amp

## Slide 20
Two-Stage CMOS Op Amp
A reference bias current I REF is generated either externally or using on-chip circuits. The current mirror formed by Q8 and Q5 supplies the differential pair Q1-Q2 with bias current. The W/L ratio of Q5 is selected to yield the desired value for the input-stage bias current I (or I/2 for each of Q1 and Q2). The input differential pair is actively loaded with the current mirror formed by Q3 and Q4.
The second stage consists of Q6, which is a common-source amplifier loaded with the current-source transistor Q7. A capacitor CC is included in the negative-feedback path of the second stage. Its function is for the frequency compensation.
The voltage gain of the first stage is to be given by:
where gm1 is the transconductance of each of the transistors of the first stage, that is, Q1and Q2.
The second stage is a current-source-loaded, common-source amplifier whose voltage gain is given by:
The dc open-loop gain of the op amp is the product of A1 and A2

## Slide 21
Two-Stage CMOS Op Amp
Capacitor Cc and transistor Qc (acting as a voltage controlled resistor) are included for Op-amp compensation to ensure stability when the Op-amp is used with feedback.
An active load realises a high-impedance load required for an amplifier. It replaces large resistors, or a large power supply voltage that would otherwise be required.

## Slide 22: Miller’s Theorem
If Av is the gain from node 1 to 2, then a floating impedance ZF can be converted to two grounded impedances Z1 and Z2.

## Slide 23: Miller Multiplication
With Miller’s theorem, we can separate the floating capacitor. However, the input capacitor is larger than the original floating capacitor. We call this Miller multiplication.

## Slide 24: Miller Multiplication(example)
Design of Analog CMOS Integrated Circuits Behzad Razavi
2nd Edition, page 190.

## Slide 25: Example: Miller Theorem

## Slide 26: Transit Frequency Calculation
prove that:
Note that fT increases with the overdrive voltage and the

## Slide 27: Example: Transit Frequency Calculation
The minimum channel length of MOSFETs has been scaled from 1 μm in the late 1980s to 65 nm in 1990s. Also, the inevitable reduction of the supply voltage has reduced the gate-source overdrive voltage from about 400 mV to 100 mV. By what factor has the fT of MOSFETs increased?
Solution:
It can be proved that Thus, the transit frequency has increased by approximately a factor of 59. For example, if μn = 400cm2/(V·s), then 65 nm devices having an overdrive of 100 mV exhibit an fT of 226 GHz.

## Slide 28
Charge-Redistribution ADCs
SAR: successive-approximation register
Its operation involves three cycles called the sample, hold, and redistribution cycles.

## Slide 29: Charge-Redistribution ADCs(examples)
If the reference voltage Vref = 8 V, what will be the voltage increment that will appear on the top plate when the switch corresponding to the least significant bit is switched
If the input voltage Vin = 3.5 V, which switches will be connected to Vref at the end of the conversion?
Set b1 = 1 (i.e. test with 100)
Therefore b1 = 0
Set b2 = 1 (i.e test with 010)
Therefore b2 = 1
Set b3 = 1 (i.e test with 011)
Therefore b3 = 1
Switches S2 and S3 are connected to Vref at the end of conversion.

## Slide 30
Flash Converters
2
2 matched resistors
Advantages:
Fastest ADC, Suitable for large bandwidth application:
  Satellite communication
  Radar processing
  Oscilloscope
Disadvantages:
High power consumption
Limited resolution(typically up to 8-bit)
Large die area(2N-1comparators)
Component matching(Comparators and resistors)

## Slide 31
Flash Converters
A resistor string creates 7 reference levels. A bank of high speed latched comparators simultaneously compares Vin against each reference level. Since the input sampling and latching take place during the first phase of the clock period, and decoding during the second phase, the entire conversion takes only one clock cycle, so this ADC is the fastest possible.
If the reference voltage for the ADC is 4 V, specify the actual reference voltage levels used in the conversion process.

## Slide 32
Common-centroid layout of a differential pair

## Slide 33: Split of Transistors
M1
M2
M3
M4
M11
M5
M7
M9
M6
M8
M10
30
30
80
80
MN
60
60
16
16
40
40
24
24
20
2
3
3
6
6
25
38
5
2
5
3
3
2
MP
Folded Cascode OPAMP

## Slide 34: Stack Design
M1
M2
M3
M4
M11
M5
M7
M9
M6
M8
M10
MN
2
3
3
6
6
5
2
5
3
3
2
MP
10x2
555555344PP334666666
11221122112211221122
22112211221122112211
777779xxoo99nno88888
X=11; o=10

## Slide 35: Resistance thermal noise of multiple fingers(example)
Design of Analog CMOS Integrated Circuits Behzad Razavi
2nd Edition, page 737

## Slide 36
C1
TC1
C5
TC5
C2
TC2
C3
TC3
C4
TC4
C2 = C1
C3 = 2C1
C4 = 4C1
C5 = 8C1
Common Centroid Structures
TC5
TC4
TC1
TC2
TC3

## Slide 37
A simplified layout of a capacitor array

## Slide 38
The circuit of Fig. 19.37(a) is designed for a nominal gain of C1/C2 = 8. How should C1 and C2 be laid out to ensure precise definition of the gain?
Solution
We form C1 as 8 unit capacitors, each equal to C2, and place all of the units in a square array [Fig. 19.37(b)]. Note that (1) C2 is symmetrically surrounded by the units comprising C1 so that the effect of vertical or horizontal gradients is canceled to the first order; and (2) dummy capacitor units are placed around the main array, creating approximately the same environment for the units of C1 as that seen by C2.
Common Centroid Structures(examples)
Behzad Razavi, “Design of Analog CMOS Integrated Circuits, 2nd Edition”, Chap. 19 Layout and Packaging, page 752.

## Slide 39: Integrated Resistor Cross-section
A resistor is made of a strip of resistive layer.
r = resistivity (W*m)
R = sheet resistance (W/)
 is a dimensionless unit(!)
The endings resistance can be significant!

## Slide 40
Diffusion/Well Resistors

## Slide 41
Polysilicon Resistances
Conductive layers can be used to shield the conductor-oxide-
conductor structure

## Slide 42
Interdigitized and Common Centroid
121212212121
R1
R2
R1
R2